## Slide 1
Insert your text Here
Insert your text Here
Insert your text Here
Insert your text Here
Insert your text Here
Realizing 5G ORAN with USRP N321: A Software – Defined
Radio Approach
Supervisor : Dr. T Nagarjuna
Abstract
Background
Methods
Expected Outcome
Future Perspectives
Impact on Society
Team members: P. Prudvi reddy, MC. Mokshith, B. Gopal
Conclusion
The growing demand for private 5G networks is driven by the need for high-speed, low-latency, and reliable wireless communication in industries such as manufacturing, healthcare, smart cities, and autonomous systems. This project focuses on the design, deployment, and performance evaluation of a scalable 5G private network using USRP N321, integrating srsRAN 5G, srsRAN 4G, and OpenAirInterface (OAI) to establish an open, flexible, and cost-effective ORAN-based solution.The architecture is built using a CU-DU split, where the Central Unit (CU) handles higher-layer network processing while the Distributed Unit (DU) manages real-time radio communications. The system utilizes ZeroMQ for efficient inter-component communication, ensuring low-latency and high-throughput data exchange. Grafana-based monitoring is implemented to track network performance metrics, including throughput, latency, signal integrity, and resource utilization. The project also evaluates single and multiple UEs, verifying network scalability, stability, and efficiency under varying load conditions.The research explores 5G ORAN implementation challenges, software-defined radio (SDR) integration, and network optimization techniques to improve reliability and adaptability for real-world applications. The findings demonstrate the feasibility of deploying private 5G networks using open-source frameworks, contributing to advancements in enterprise networking, industrial automation, and next-generation communication technologies.
5G Open RAN (ORAN) is revolutionizing wireless communication by enabling vendor-neutral, software-driven networks. Unlike traditional proprietary solutions, ORAN disaggregates hardware and software, promoting flexibility, cost efficiency, and innovation. This architecture facilitates scalable private networks for industries like healthcare, smart cities, disaster management, industrial automation, and autonomous systems.5G enhances ultra-reliable low-latency communication (URLLC), massive machine-type communication (mMTC), and enhanced mobile broadband (eMBB), making it ideal for critical applications such as telemedicine, remote industrial control, real-time monitoring, and smart infrastructure.
Why 5G Instead of 4G?
Lower Latency: 5G offers sub-1ms latency, while 4G has 20-30ms, making 5G suitable for real-time applications like autonomous driving, remote surgery, and mission-critical IoT.
Higher Speed & Capacity: 5G provides speeds up to 10 Gbps, far exceeding 4G’s 1 Gbps, enabling seamless video streaming, AR/VR applications, and massive data transfers.
Massive Device Connectivity: 5G supports up to a million devices per km², whereas 4G is limited to 100,000 devices/km², making it essential for smart cities and IoT expansion.
Energy Efficiency: 5G is designed for low power consumption, extending battery life for IoT and reducing operational costs.
Network Slicing: Unlike 4G, 5G supports network slicing, allowing customized virtual networks for different applications such as emergency services, industrial automation, and public networks.
Better Spectrum Utilization: 5G operates across sub-6 GHz and mmWave bands, providing higher bandwidth and improved signal quality compared to 4G.
By adopting 5G ORAN, industries gain higher performance, flexibility, and reduced costs, fostering technological advancements, research, and reliable communication solutions for the future.
gNB (Next-Generation NodeB): Acts as the base station for the 5G network, handling radio communications with UEs.
CU-DU Split: Separates control and user plane functions for scalable and efficient 5G deployment.
USRP N321: Software-defined radio (SDR) used for implementing the gNB in the 5G ORAN setup.
ZeroMQ: Enables efficient and low-latency communication between network components.
OctoClock-G CDA-2990: Provides precise clock synchronization for accurate timing across network elements.
5G Core (5GC): Manages authentication, mobility, and data flow for connected user devices.
Grafana: Used for real-time monitoring of network performance, including latency and throughput.
A 5G ORAN network was successfully deployed using open-source frameworks and SDR-based hardware, ensuring flexibility and cost-effectiveness.
ZeroMQ-based communication was implemented to enhance low-latency and efficient data exchange between network components.
Performance testing confirmed stable connectivity and seamless operation with both single and multiple UEs.
Grafana was utilized for real-time monitoring, enabling analysis of key performance metrics such as throughput, latency, and reliability.
Future enhancements will focus on optimizing network stability, security, and scalability for large-scale deployments.
srsRAN gNB with DPDK: Implementing Data Plane Development Kit (DPDK) to improve packet processing, reduce latency, and enhance overall network efficiency.
srsRAN gNB Performance Tuning: Fine-tuning network parameters to maximize throughput, reliability, and efficiency for high-performance applications.
srsRAN gNB on Kubernetes: Deploying srsRAN gNB in a Kubernetes environment to enable scalability, automation, and cloud-native management.
Enhancing Disaster Response: Enables real-time communication and rapid deployment of emergency networks in disaster-affected areas, ensuring connectivity for rescue operations.
Affordable and Scalable Solutions: Provides a cost-effective and flexible alternative to proprietary telecom solutions, making 5G technology accessible for various industries and rural areas.
Advancing Research & Innovation: Supports academic and industrial research in open-source 5G and ORAN, driving advancements in next-generation wireless networks.
Empowering Critical Sectors: Strengthens healthcare, smart cities, and autonomous systems by offering low-latency, high-reliability connectivity for mission-critical applications.
Bridging the Digital Divide: Helps underserved communities by providing affordable, high-speed communication infrastructure, improving education, business, and public services.